# HOSPITAL:

# Respiratory Care Services Policy and Procedure Manual

| Policy and Procedure | StabilTube™ |
| --- | --- |
| Area: Respiratory Care Services | Performed by: Respiratory Care Practitioners |
| Policy Number: | Approved by: |
|  | Date: |
| Current Effective Date | Approved by: |
|  | Date: |
| Review Date | Approved by: |
|  | Date: |
| Revised Date | Approved by: |
|  | Date: |

POLICY

This policy assures the standardized of use of the StabilTube™ Long Term Endotracheal Tube Holder for securing the endotracheal tube in the pediatric, adolescent and adult patient.

PURPOSE

The purpose is to provide an easy implemented protocol to be used by the Respiratory Care Practitioner with effective guidelines and consistent instruction for use and application of the StabilTube™ for securing the endotracheal tube.

DEFINITION

To ensure patient safety, the patient with a temporary, artificial translaryngeal airway should have the fixation device secured at the earliest appropriate time.

SETTINGS

The endotracheal tube should be placed and secured in an environment in which the patient can be physiologically monitored and in which emergency equipment and appropriately trained health care providers with airway management skills are immediately available.

EQUIPMENT

B&B StabilTubeTM (includes StabilTube Endotracheal Tube Holder, Skin-Prep™, Releasable Cable Tie and Blue Tie Cap), Alcohol Swabs, Bandage Scissors, Skin and Oral Care Supplies, Suction setup with an appropriate size catheter and an oral suction attachment. Use of the B&B Universal Bite Block™ or the B&B Bite Proof Bite Block™ is recommended with the StabilTube.

.

Skin Prep™ is a registered trademark of Smith & Nephew.

VELCRO® brand is a Registered Trademark of VELCRO Industries B.V.

PROCEDURE

A: Application/Preparation Steps

1.  	Note endotracheal tube placement at either the nare or teeth/gum line and compare with 	existing charting as to proper depth. If this is a new endotracheal tube placement, 	auscultate to assure bilateral breath sounds and a proper reading using an ETCO2 	device. If possible, ascertain tube placement with an X-Ray prior to securing with the 	releasable endotracheal tube Cable Tie.

2.  	Clean the patient’s face to remove all secretions & moisture from the application areas. 	Application areas are either the area between the nose & upper lip laterally along the 	face to beneath the ear lobes or the area over the bridge of the nose and cheek area.

3.  	Clean the endotracheal tube from point of placement to its distal end to remove all 	moisture and secretions.

4.  	Wipe & clean both application areas on the face and the endotracheal tube with an 	alcohol prep pad and fan dry the areas.

5.  	Place the endotracheal tube in the appropriate position in the mouth. Positioning of the 	endotracheal tube must be changed in the mouth, from side to center to side every tape 	change to prevent tissue erosion and facilitate oral care.

B: Application/Action Steps

1. 	Apply a skin barrier to the area on the face in which you will apply the adhesive. Apply 	Skin PrepTM to both the facial skin and endotracheal tube application areas. Fan dry for 	at least 25 seconds.

2. 	The adhesive application areas include the following:

a. Oral Application securing to the Upper Lip: prep the area between the nose & upper 	lip laterally along the face,

b. Nasal Application, prep the area over the bridge of the nose and cheek area.

c. Endotracheal tube, prep at point of securement.

3. 	Place the ET Tube in the appropriate position in the mouth. Positioning is recommended 	to be changed in the mouth from Left of Center to Right of Center every tape change to 	prevent tissue erosion and to facilitate oral care.

4.	Place the Cable Tie over the head of the endotracheal tube (Figure 1). Remove the 	release liner from the face piece and the T-Tab (Figure 2/Figure C).

5.	Apply Face Piece and T-Tab (Figure 3) on the desired prepped area of the face and tube 	with Cable Tie (Figure B) centered over the endotracheal tube.

6.	Check that the endotracheal tube is at the proper centimeter marking with the 	appropriate anatomical landmark. Apply adhesive back of the T-Tab to the endotracheal 	tube. Secure the retaining unit tight, ½ inch above the identification marking on the tube. 	For maximum securing ability, do not place anything between the retaining unit and the 	endotracheal tube.

7. 	Peel the remainder of the backing, and place over the lip for oral intubation, over the 	bridge of the nose for nasal intubation.

8. 	Pass the Elastic VELCRO® brand neck band (Figure 4) under the earlobe & behind the 	patient's head, around the neck, and by the other earlobe. Take the VELCRO® brand 	leading edge of the Neck band and pass it through the Buckle D-Ring and fasten (Figure 	5). Be sure to pull the neck band snug so that only one finger can be inserted between 	the neck band and the patient's neck.

9.	Smooth the VELCRO® brand section to assure maximal engagement of the VELCRO® 	brand 	with the neck band material.

10.	Firmly apply pressure with a smoothing action to ALL adhesive areas that have contact 	with skin.

11. 	After the endotracheal tube position is confirmed, trim off the excess Cable Tie tab 	beyond 1/2 inch above the retaining unit (Figure 6). Place the Blue Cap on the cut end of 	the Cable Tie.

12.	Periodically inspect the device for proper adhesion and the Cable Tie for secure 	retention.

13. 	To release the Cable Tie, grasp the head of the Cable Tie and the ET Tube and remove 	the Blue Cap. Deflect the release and push the excess tab through the cable port.

.

# C: Documentation

Chart the Time, Date, endotracheal tube size and cm marking at the appropriate 	anatomical landmarks on the hospital documentation Flow Sheet.

D. Adjusting, Changing &/or Removal of StabilTubeTM

1.	To adjust the depth of the endotracheal tube, release the Cable Tie around the 	endotracheal tube. Firmly hold the endotracheal tube once the Cable Tie is loosened to 	prevent accidental extubation. Adjust the position of the endotracheal tube, confirm 	position and re-secure the Cable Tie around the endotracheal tube.

2.	To adjust the tightness of the neck band, or to provide skin care, release the VELCRO 	section of the neck band & adjust to appropriate tightness. To completely remove pass 	the VELCRO tip through the Buckle.

3.	To remove the StabilTubeTM, release and completely open the Cable Tie from the 	endotracheal tube.  Firmly hold the endotracheal tube once the Cable Tie is loosened to 	prevent accidental extubation.

4.	Wash and provide the patient's face and neck with the appropriate skin care.

F: Precautions/Adverse Effects

1.	Possible Adverse effects are tube slippage and possible inadvertent extubation.

2.  	Periodically inspect the StabilTube and patient Q-shift, prn or more frequently.  In the 	event the patient is diaphoretic, has copious oral secretions, loss of adhesion on the 	patient’s face or endotracheal tube may occur, immediately replace the StabilTube. A 	spare is recommended at the bedside.

3.  	Periodically inspect the space between the neck band of the tape and the patient's neck. 	It should be snug enough to only allow one finger to be inserted. If it is too tight or too 	loose, adjust the neck band immediately.

4. 	Periodically inspect the skin area under the adhesive backing to help prevent injury to 	the lips and underlying tissues due to unrelieved pressure.

5.	Never use Benzoin or other adhesive enhancing product in conjunction with this or any 	other Acrylic Hypo-Allergenic Adhesive product.  Always use the Skin barrier provided.

6.  	After providing skin care, make sure the adhesive contact areas are completely dry 	and not oily.

7.	The StabilTube should not be used by persons shown to be allergic to the adhesive.

8.  	Do not wrap the Pilot Balloon Tube in the loop with the Cable Tie.

9.	Do not pull the Cable Tie tight with any other device except two fingers. If pulled too tight 	the endotracheal tube may hourglass and alter the inner diameter of the endotracheal 	tube. This can be noted by a significant dip in the endotracheal tube surface on either 	side of the Cable Tie.

10. 	Support the ventilator tubing to reduce pressure on the endotracheal tube.

11.	The StabilTube is intended for single patient use.

Figure A

Figure B                                        Figure C

Releasable Cable Tie

Figure D

Figure 1  					Figure 2

Figure 3   					  Figure 4

Figure 5   					 Figure 6

REFERENCES

1.	AARC Clinical Practice Guideline/Management of Airway Emergencies

Respir Care 1995; 40(7):749-760)

2.	AARC Clinical Practice Guideline/Removal of the Endotracheal Tube

Respir Care 1999; 44(1):85-90)

3. 	2005 American Heart Association Guidelines for Cardiopulmonary Resuscitation and 	Emergency Cardiovascular Care. Part 7.1: Adjuncts for Airway Control and Ventilation. 	Circulation 2005; 112: IV-51-IV-57.

# Text boxes

Buckle D- Ring

Cable Tie

Face Piece

T-Tab

Release Liner